## Slide 1
Chapter 9: Transport Layer and Security Protocols for Ad Hoc Wireless Networks
Introduction
Issues
Design Goals
Classifications
TCP Over Ad Hoc Wireless Networks
Other Transport Layer Protocols
Security in Ad Hoc Wireless Networks
Network Security Requirements
Issues and challenges in security
Network security attacks
Key Management
Secure Routing

## Slide 2: Introduction
The objectives of a transport layer protocol include setting up of:
  End-to-end connection
  End-to-end delivery of data packets
  Flow control
  Congestion control
Transport layer protocols
  User datagram protocol (UDP): unreliable and connection-less transport layer protocols
  Transmission control protocol (TCP): reliable, byte-stream-based, and connection-oriented transport layer protocols
These traditional wired transport layer protocols are not suitable for ad hoc wireless networks.

## Slide 3: Issues
Issues while designing a transport layer protocol for ad hoc wireless networks:
  Induced traffic refers to the traffic at any given link due to the relay traffic through neighboring links.
  Induced throughput unfairness refers to the throughput unfairness at the transport layer due to the throughput/delay unfairness existing at the lower layers such as the network and MAC layers.
  Separation of congestion control, reliability, and flow control could improve the performance of the transport layer.
  Power and bandwidth constraints affects the performance of a transport layer protocol.
  Misinterpretation of congestion occurs in ad hoc wireless networks.
  Completely decoupled transport layer needs to adapt to the changing network environment.
  Dynamic topology affects the performance of a transport layer.

## Slide 4: Design Goal
The protocol should maximize the throughput per connection.
It should provide throughout fairness across contending flows.
It should minimize connection setup and connection maintenance overheads.
The protocol should have mechanisms for congestion control and flow control in the network.
It should be able to provide both reliable and unreliable connections.
The protocol should be able to adapt to the dynamics of the network.
One of the important resources must be used efficiently.
The protocol should be aware of resource constraints.
The protocol should make use of information from the lower layer.
It should have a well-defined cross-layer interaction framework.
The protocol should maintain end-to-end semantics.

## Slide 5: Classification of Transport Layer Solutions
Transport Layer Solutions for Ad Hoc Wireless Networks
Split Approach
Other transport layer approach
End-to-end
approach
Split-TCP
ACTP
ATP
TCP-ELFN
TCP-F
TCP-Bus
ATCP
TCP over ad hoc wireless networks

## Slide 6: TCP over Ad Hoc Wireless Networks
TCP taking 90% of the traffic is predominant in the Internet.
This chapter focuses on TCP extension in ad hoc wireless networks.
Transport protocol should be independent of the network layer technology, e.g., no matter fiber or radio is used
But TCP is optimized for wired network  Congestion control
  TCP assumes timeout is due to congestion
  Wireless links are not reliable, packet loss may be as high as 20%
  In wired network, packet loss is due to congestion  slow down
  In wireless network, due to wireless links  try harder

## Slide 7: Why does TCP not perform well in Ad Hoc Wireless Networks
Misinterpretation of packet loss
Frequent path breaks
Effect of path length
Misinterpretation of congestion window
Asymmetric link behavior
Uni-directional path: TCP ACK requires RTS-CTS-Data-ACK exchange
Multipath routing
Network partitioning and remerging
The use of sliding-window-based transmission

## Slide 8: TCP Over Ad Hoc Wireless Network
Feedback-based TCP (TCP Feedback – TCP-F)
  Requires the support of a reliable link layer and a routing protocol that can provide feedback to the TCP sender about the path breaks.
  The routing protocol is expected to repair the broken path within a reasonable time period.
  Advantages: Simple, permits the TCP congestion control mechanism to respond to congestion
  Disadvantages:
    If a route to the sender is not available at the failure point (FP), then additional control packets may need to be generated for routing the route failure notification (RFN) packet.
    Requires modification to the existing TCP.
    The congestion window after a new route is obtained may not reflect the achievable transmission rate acceptable to the network and the TCP-F receiver.

## Slide 9: TCP Over Ad Hoc Wireless Network
TCP with explicit link failure notification (TCP-ELFN)
  Handle explicit link failure notification
  Use TCP probe packets for detecting the route reestablishment.
  The ELFN is originated by the node detecting a path break upon detection of a link failure to the TCP sender.
  Advantages:
    improves the TCP performance by decoupling the path break information from the congestion information by the use of ELFN.
    Less dependent on the routing protocol and requires only link failure notification
  Disadvantages
    When the network is partitioned, the path failure may last longer
    The congestion window after a new route is obtained may not reflect the achievable transmission rate acceptable to the network and TCP receiver.

## Slide 10: TCP Over Ad Hoc Wireless Network
TCP with buffering capability and sequence information (TCP-BuS)
  Use feedback information from an intermediate node on detection of a path break.
  Use localized query (LQ) and REPLY to find a partial path
  Upon detection of a path break, an upstream intermediate node originates an explicit route disconnection notification (ERDN) message.
  Advantages
    Performance improvement and avoidance of fast retransmission
    Use on-demand routing protocol
  Disadvantages
    Increased dependency on the routing protocol and the buffering at the intermediate nodes
    The failure of intermediate nodes may lead to loss of packets.
    The dependency of TCP-BuS on the routing protocol many degrade its performance.

## Slide 11: TCP Over Ad Hoc Wireless Network
Ad Hoc TCP (ATCP)
  uses a network layer feedback mechanism to make the TCP sender aware of the status of the network path
  Based on the feedback information received from the intermediate nodes, the TCP sender changes its state to the persist state, congestion control state, or the retransmit state.
  When an intermediate node finds that the network is partitioned, then the TCP sender state is changed to the persist state.
  The ATCP layer makes use of the explicit congestion notification (ECN) for maintenance for the states.
  Advantages
    Maintain the end-to-end semantics of TCP
    Compatible with traditional TCP
    Provides a feasible and efficient solution to improve throughput of TCP
  Disadvantages
    The dependency on the network layer protocol to detect the route changes and partitions
    The addition of a thin ATCP layer to the TCP/IP protocol changes the interface functions currently being used.

## Slide 12: TCP Over Ad Hoc Wireless Network
Split-TCP
  provides a unique solution to the channel fairness problem by splitting the transport layer objectives into congestion control and end-to-end reliability.
  Splits a long TCP connection into a set of short concatenated TCP connections with a number of selected intermediate nodes as terminating points of these short connections.
  Advantages
    Improved throughput
    Improved throughput fairness
    Lessened impact of mobility
  Disadvantages
    It requires modifications to TCP protocol.
    The end-to-end connection handling of traditional TCP is violated.
    The failure of proxy nodes can lead to throughput degradation.

## Slide 13: Other Transport Layer Protocols
Application controlled transport protocol (ACTP)
  A light-weight transport layer protocol and not an extension to TCP.
  ACTP assigns the responsibility of ensuring reliability to the application layer.
  ACTP stands in between TCP and UDP where TCP experiences low performance with high reliability and UDP provides better performance with high packet loss in ad hoc wireless networks.
  Advantages
    Provides the freedom of choosing the required reliability level to the application layer.
    Scalable for large networks
    There is no congestion window
  Disadvantages
    It is not compatible with TCP.
    Could lead to heavy congestion

## Slide 14: Other Transport Layer Protocols
Ad hoc transport protocol (ATP)
  specifically designed for ad hoc wireless networks and is not a variant of TCP and differ from TCP in the following ways:
    Coordination among multiple layers
    Rate based transmissions
    Decoupling congestion control and reliability
    Assisted congestion control
  ATP uses information from lower layers for
    Estimation of the initial transmission rate
    Detection, avoidance, and control of congestion
    Detection of path breaks
  Advantages: improved performance, decoupling of the congestion control and reliability mechanisms, and avoidance of congestion window fluctuations
  Disadvantages
    The lack of interoperability with TCP
    Fine-grained per-flow timer may cause the scalable problem