## Slide 1: Nuclear Fusion Powers the Universe
Two nuclei combine into one nucleus plus a nucleon is called nuclear fusion, a nuclear reaction.
The picture here illustrates the fusion of
2D + 3T  4He + n
that releases a lot of energy.
Neutron proton

## Slide 2: Nuclear Fusion in Stars
Stars are giant fusion reactors.
Nuclear fusion reactions provide energy in the Sun and other stars. Solar energy drives the weather and makes plants grow.
Energy stored in plants sustains animal lives, ours included.
The solar system
Solar system NASA
These links may move

## Slide 3
The Sun
Core: Radius = 0.25 Rsun T = 15 Million K Density = 150 g/cc
Envelope: Radius = Rsun = 700,000 km T = 5800 K Density = 10-7 g
Life of Star: tug-of-war between Gravity & Pressure

## Slide 4: Controlled Nuclear Fusion Energy for D-T Fusion
Estimate the fusion energy for D + T  4He + n
Estimate the fusion energy Q
The mass excess (MeV) are given below every species.
D + T  4He + n + Q 13.136 + 14.950 = 2.425 + 8.070 + Q Q = 17.6 MeV/fusion
This amount is 3.5 MeV/amu compared to 0.8 MeV/amu for fission.
Estimating Q is an important skill. Mass and mass excess can be used, the latter is usually given to unstable nuclides.

## Slide 5: Controlled Nuclear Fusion Energy for Fusion Reactions
Common fusion reactions and their Q values
H + H  D + + + n + 1.44 MeV
D + T  4He + n + 17.6 MeV
D + 3He  4He + p + 18.4 MeV
D + D  3He + n + 3.3 MeV
D + D  3T + p + 4.0 MeV
See Interactive Plasma Physics Education Experience : http:// ippex.pppl.gov/

## Slide 6: Nuclear Fusion and Plasma
D and T mixtures have to be heated to 10 million degrees. At these temperatures, the mixture is a plasma.
A plasma is a macroscopically neutral collection of charged particles.
Ions (bare nuclei) at high temperature have high kinetic energy and they approach each other within 1 fm, a distance strong force being effective to cause fusion.

## Slide 7: How can we capture the potential of fusion energy?
A fuel at 108 K cannot be contained in a furnace as in conventional thermo-electric power stations
  All materials are plasmas (ionized gas) at this temperature
Two alternatives
  Contain the fuel in a magnetic field
    Charged particles move in circles around magnetic field lines
    Magnetic confinement fusion (MCF), magnetic fusion energy (MFE), or magnetic fusion
  Let the fuel expand freely in the centre of a chamber
    Inertial confinement fusion (ICF), inertial fusion energy (IFE) or inertial fusion

## Slide 8: Nuclear Fusion and Plasma
by confining it long enough that a sufficient number of fusion reactions can
take place.
How much energy can be produced in such a confined plasma? The
energy produced per time τ depends on the kinetic energy Q of the reaction How much energy can be produced in such a confined plasma?
energy produced per time τ depends on the kinetic energy Q of the reaction

## Slide 9: Nuclear Fusion and Plasma

## Slide 10: Nuclear Fusion and Plasma

## Slide 12
Until ignition is achieved the plasma has to be heated externally. There
are three different heating mechanisms used: ohmic heating, heating by
high-frequency waves, and by the injection of beams of neutral particles.

## Slide 13: Nuclear Fusion and Plasma - particle motion
Charged particles avoid crossing magnetic lines.

## Slide 14: Nuclear Fusion using Magnetic Plasma Confinement
A plasma distorts magnetic field or bends magnetic lines.
A Magnetic Bottle for Plasma Confinement

## Slide 15
magnetic confinement device, : to trap high temperature plasma using magnetic fields. In a magnetic mirror a specially shaped electromagnet creates a configuration of magnetic field lines which reflects charged particles from a high density magnetic field region to a low density magnetic field region.
Large experimental magnetic mirror machines have been developed to confine hot deuterium plasma as a possible approach to fusion power, since the plasma is too hot for any solid container.
A charged particle moving within a region of magnetic field experiences a Lorentz force that causes it to move in a helical (corkscrew) path along a magnetic field line. The radius of the circle that the particle describes is called the radius of gyration or gyro-radius.
If it enters a region of denser magnetic field lines, a field gradient, the combination of the radial component of the fields and the azimuthal motion of the particle results in a force pointed against the gradient, in the direction of lower magnetic field. It is this force that can reflect the particle, causing it to decelerate and reverse direction

## Slide 16: Inertial Fusion
NIF Lawrence Livermore National Laboratory

## Slide 17: Plasma Conditions During ICF
Before compression and ignition Density: solid DT pallet at 0.225 g/cm3 and gas Temperature: few Kelvin
During the burn phase Density: 300 to 1000 times solid density 300 to 1000 g/cm3 ≈ 1026 cm-3 Temperature: around 10.000.000 K or 10 keV Pressure: around 1012 bar
Confinement time needed: around 200 ps

## Slide 18: The Concept
Inertial Fusion relies on extracting fusion energy from a freely expanding plasma in a series of micro-explosions
There is no confinement, but by analogy with magnetic (confinement) fusion the “confinement” time is determined by inertia
  After this time cooling due to expansion will lead to a rapid drop in the fusion reaction rate

## Slide 19: Requirements
Assuming constant density and temperature during the confinement time and no reactions afterwards the burn fraction at 10 keV (kT/e, 108 K) is given by:
  Numerical modelling gives a burn parameter of 7 g cm-2 provided that R > 1.5 g cm-2, below this f falls rapidly
A containable yield requires a mass < 10 mg therefore R > 6 g cm-2 requires  > 300 g cm-3
  1000 times solid density (atoms m-3)
  The need for such astronomical densities is the major challenge of inertial fusion

## Slide 20: Achieving High Densities
A hollow sphere ~ mm in diameter is compressed by heating the outside to produce an expanding plasma that acts like a rocket propelling the shell inwards
  The inside must remain degenerate in order to minimize the pressure (~ 790 eV at 300 g cm-3 giving ~ 30 Gbar)
  Compression time ~ 10-8 s
  Minimum absorbed energy ~ 100 kJ

## Slide 21: Achieving High Temperatures
If the implosion velocity exceeds 105 m s-1 then the collision of the walls at the centre leads to temperatures sufficient to start fusion reactions and the alpha particles heat the rest of the plasma

## Slide 22
Controlling Fusion using Inertia

## Slide 23
Direct Drive:
Laser Beams are focused onto the
surface of the target ( pellet of fuel)
Indirect Drive
Laser Beams are focused at the
inner site of the cylinder
NATIONAL IGNITION FACILITY
Target, filled with a deuterium tritium (D-T) mixture
Laser Beam
cylindrical hohlraum made of gold
Target
In this approach, multiple laser beams with a 20 ns duration precisely shaped pulse are arranged in cones about the axis of a high-Z cylindrical hohlraum.
A hohlraum is a hollow, cylinder-shaped device that is used to focus and control radiation.
Inertial Confinement Fusion
HiPER